SERIAL PROTOCOL

This document describes how to communicate with a Lutron RadioRa Lighting Controller via the serial port.

Rear Serial Port Pinout for the Lutron RadioRa Controller

Purpose

| PIN | PURPOSE | DB9 - Female |
| --- | --- | --- |
| 1 | Not Used |  |
| 2 | Receive |  |
| 3 | Transmit |  |
| 4 | Not Used |  |
| 5 | Ground |  |
| 6 | Not Used |  |
| 7 | Not Used |  |
| 8 | Not Used |  |
| 9 | Not Used |  |

Rear Serial Port Settings for the Lutron RadioRa Controller

Parameter Value

| PARAMETER | VALUE |
| --- | --- |
| Baud | 9600 |
| Data Bits | 8 |
| Stop Bits | 1 |
| Parity | None |
| Flow Control | None |

For connection to the Xantech MRC-88

Connection to the rear serial port requires a male to male standard straight through serial cable (no null modem required). It is recommended that the RS-232 cable be 25 feet or less.

For connection to the SmartPAD LCD touch panel

(NOTE: Requires the RS422232 module with 781RG power supply)

Connection to the rear serial port requires a male to female NULL MODEM serial cable. It is recommended that the RS-232 cable be 25 feet or less.

For connection to the Xantech RS2321X8 Serial Router

Connection to the RS232 serial ports requires a male to male standard straight through serial cable (no null modem required). Connection to the RS422 serial ports requires the RS422232 module with 781RG power supply and a male to female NULL MODEM serial cable. It is recommended that the RS-232 cable be 25 feet or less.

Programming the Lutron RadioRa controller

In the Dragon Drop software you will need to build the command by sending 5 of the RS-232 commands in the following order:

Button

State

System

For example to turn “press” button 1 on system 1 you would send:

Button 01

State ON

System 1

You must send the System Command even if you are only using 1 system. The above command represents a single command being sent to the Lutron RadioRa lighting controller. All three lines are required to send one single command. Here is the example above in Dragon Drop-IR MRC software: