SERIAL PROTOCOL

This document describes how to communicate with a Pioneer PRO-1110HD Plasma Display via the serial port.

Rear Serial Port Pinout for the Pioneer Plasma Display

Purpose

| PIN | PURPOSE | DB9 - Male |
| --- | --- | --- |
| 1 | Not Used |  |
| 2 | Receive |  |
| 3 | Transmit |  |
| 4 | DTR |  |
| 5 | Ground |  |
| 6 | DSR |  |
| 7 | RTS |  |
| 8 | CTS |  |
| 9 | Not Used |  |

Rear Serial Port Settings for the Pioneer Plasma Display

Parameter Value

| PARAMETER | VALUE |
| --- | --- |
| Baud | 9600 |
| Data Bits | 8 |
| Stop Bits | 1 |
| Parity | Odd |
| Flow Control | None |

For connection to the Xantech MRC-88

Connection to the rear serial port requires a female to male standard straight through serial cable (no null modem required). It is recommended that the RS-232 cable be 25 feet or less.

For connection to the SmartPAD LCD touch panel

(NOTE: Requires the RS422232 module with 781RG power supply)

Connection to the rear serial port requires a female to female NULL MODEM serial cable. It is recommended that the RS-232 cable be 25 feet or less.

For connection to the Xantech RS2321X8 Serial Router

Connection to the RS232 serial ports requires a female to male standard straight through serial cable (no null modem required). Connection to the RS422 serial ports requires the RS422232 module with 781RG power supply and a female to female NULL MODEM serial cable. It is recommended that the RS-232 cable be 25 feet or less.